Autodesk® Inventor® Files
# General
Autodesk® Inventor® (AI) uses the OLE compound file format (OLECF).
It consists of:
1. Common properties stored as the ‘[5]’ + generic name in the root folder of the OLECF.
2. The iPoroperties (ref. “2 iProperties”) of the inventor file are stored likewise as the common properties.
3. The model data (ref. “3 RSeStorage”) itself consists of three parts:
  1. The data segments RSeSegInfo and the database RSeDb
  2. The data sections in RSeStorage (Mxxx & Bxxx)
  3. Embedded additional documents
A typical content looks like (this information can be retrieved by an appropriate reader, e.g. 7Zip):
Samples_2015\Arm_Rest.ipt\
[5]Aaalpg0m0wzvuhc41dwauxbwJc	size: 236
[5]PypkizqiUjudbposAayal4qdGf	size: 912
[5]Qm0qv30hP3udrkgvAaitm1o20d	size: 776
[5]Qz4dgm1gRjudbpksAayal4qdGf	size: 428
[5]Ynltsm4aEtpcuzs1Lwgf30tmXf	size: 884
[5]Zrxrt4arFafyu34gYa3l3ohgHg	size: 6016
UFRxDoc	size: 1567
RSeStorage\
M4hdhqvewibltjmqsunj4ya2afb	size: 1048
B4hdhqvewibltjmqsunj4ya2afb	size: 255373
Mhmni6ockdkoqujh2mxuct6xpjh	size: 1640
Bhmni6ockdkoqujh2mxuct6xpjh	size: 21551
Mifbzpuh4ctvlotegfsujztk5fi	size: 3157
Bifbzpuh4ctvlotegfsujztk5fi	size: 6854
Mkbgibsb63qppc3mtnfg1mgrrjk	size: 702
Bkbgibsb63qppc3mtnfg1mgrrjk	size: 58
Mlkvspscpp4sptk31nakvior1jn	size: 417
Blkvspscpp4sptk31nakvior1jn	size: 62
Mokzp5gex6iz2d64rfz6zt6e5nc	size: 5023
Bokzp5gex6iz2d64rfz6zt6e5nc	size: 223163
Mpzeofgedjksrqvhz4y6o2t3ebi	size: 4183
Bpzeofgedjksrqvhz4y6o2t3ebi	size: 794634
Mrwgbh6erh4kia54m4kpqphjcji	size: 988
Brwgbh6erh4kia54m4kpqphjcji	size: 892
Muh4bwjcv4p4ltrzsut1linfmfb	size: 560
Buh4bwjcv4p4ltrzsut1linfmfb	size: 78084
Muuj3behly6acab5ve6jwgp1tbh	size: 2163
Buuj3behly6acab5ve6jwgp1tbh	size: 2381
RSeDbRevisionInfo	size: 12587
RSeSegInfo	size: 10698
V43/
RSeDb	size: 638
RSeEmbeddings/
Contents	size: 319
DatabaseInterfaces	size: 509
Embedding 3/
[1]CompObj	size: 80
[1]Ole	size: 20
[1]Ole10Native	size: 10170
# iProperties
Each property has a number and a value. Values not mentioned are not known but may exist. Each property set has:
ID	Name	Type	Description
0x01	Code Page	Number	The number of the code page, normally UTF-16LE
0xFF	Name	String	The name of the property set.
0x80000000	Language code	Number	The ISO 639-1 language code

## Inventor Document Summary Information
Filename:	'[5]Aaalpg0m0wzvuhc41dwauxbwJc'
Clas-ID:	{D5CDD502-2E9C-101B-9397-08002B2CF9AE}
Additional to the common properties:
ID	Name	Type	Description
0x02	Category	String	The category of the document
0x0E	Manager	String	The manager of the document
0x0F	Author	String	The author of the document

## Inventor Summary Information
Filename:	'[5]Aaalpg0m0wzvuhc41dwauxbwJc'
Clas-ID:	{F29F85E0-4FF9-1068-AB91-08002B27B3D9}
Additional to the common properties:
ID	Name	Type	Description
0x02	Title	String	The title of the document
0x03	Subject	String	The subject of the document
0x04	Author	String	The author of the document
0x05	Keywords	String	The set of keywords for the document
0x06	Comment	String	The comment for the document
0x08	Last Saved By	String	The name of the user who saved the document the last time
0x09	Revision	String	The revision number
0x11	Thumbnail	IPictureDisp	The thumbnail for the document.

## Design Tracking Properties
Filename:	'[5]PypkizqiUjudbposAayal4qdGf'
Clas-ID:	{32853F0F-3444-11D1-9E93-0060B03C1CA6}
Additional to the common properties:
ID	Name	Type	Description
0x08	Last Saved By	String	The name of the user who saved the document the last time
0x04	Creation Time	Date	The timestamp the file was created
0x05	Part Number	String	The number of the part
0x07	Project	String	The name of the project
0x09	Cost Center	String	The name of the cost center
0x0A	Checked By	String	The user who did the check
0x0B	Date Checked	Date	The timestamp when it was checked
0x0C	Engr Approved By	String	The user who approved the engineering
0x0D	Engr Date Approved	Date	The timestamp when it was approved
0x11	User Status	String	The status of the document
0x14	Material	String	The material of the part
0x15	Part Property Revision Id	String
0x17	Catalog Web Link	String	Link to the catalog in the web
0x1C	Part Icon	IPictureDisp	The thumbnail of the part
0x1D	Description	String	The description of the part
0x1E	Vendor	String	The name of the vendor
0x1F	Doc. SubType	String	The internal name of the document’s sub type
0x20	Doc. SubType Name	String	The name of the document’s sub type
0x21	Proxy Refresh Date	Date
0x22	Mfg Approved By	String
0x23	Mfg Date Approved	Date
0x24	Cost	Currency
0x25	Standard	String
0x28	Design Status	Long
0x29	Designer	String
0x2A	Engineer	String
0x2B	Authority	String
0x2C	Parameterized Template	Boolean
0x2D	Template Row	String
0x2E	External Property Revision Id	String
0x2F	Standard Revision	String
0x30	Manufacturer	String
0x31	Standards Organization	String
0x32	Language	String
0x33	Defer Updates	Boolean
0x34	Size Designation
0x38	Categories	String
0x37	Stock Number	String
0x39	Weld Material	String
0x43	Inventor Version	String	The version of the creating Inventor application
0x47	Inventor Material	String	Path to the default material
0x48	Inventor Default	String	???

## _Private Model Information
Filename:	'[5]Qm0qv30hP3udrkgvAaitm1o20d'
Clas-ID:	{}
Additional to the common properties:
ID	Name	Type	Description
0x08	Flags1: Length units	Number	0101 = millimeter / 1000 = inch
0x09	Flags2: angle units	Number	0 = grad, 1 = radiant
0x0A	Flags3: time units	Number	0 = second, 1 = minute
0x0B	Flags4: mass units	Number	BIT 0: 0 = grad, 1 = radiant / BIT 1-4: b001 = kg, b010 = gram, b011 = lb
0x0C	Flags5: decimal places for length	Number	Factor = 1e-[value]
0x0D	Flags6: decimal places for angles	Number	Factor = 1e-[value]
0x0E	Compacted	Boolean
0x0F	AssemblyAvailablePvs
0x10	PartActiveColorStyle	XML

## Design Tracking Control
Filename:	'[5]Qz4dgm1gRjudbpksAayal4qdGf'
Clas-ID:	{}
Additional to the common properties:
ID	Name	Type	Description
0x0D	Next number	String
0x0E	Current number	String
0x0F	Previous number	String
0x10	Revision User	String
0x11	Revision date	Date
0x12		UUID
0x15		UUID
0x16		Number

## Inventor User Defined Properties
Filename:	'[5]Ynltsm4aEtpcuzs1Lwgf30tmXf'
Clas-ID:	{}
The list of user defined properties.
# RSeStorage
The folder contains the data of the file. The root entry is the database ‘RSeDb’. The segment information, introduced with Inventor 2003, is stored in a separate file (‘RSeSegInfo’) from 2009 on.
In this chapter a set of datatypes are used.
Name	Number of Bits	Description
UInt8	8	Unsigned byte
SInt8	8	Signed byte
UInt16	16	Unsigned word
SInt16	16	Signed word
UInt32	32	Unsigned integer
SInt32	32	Signed integer
UUID	128	4-2-2-2-6 Bytes the internal “internal name”
Date	64	Timestamp in milliseconds starting form (1.1. 1601)
String16	32+length*16	UTF-16LE encoded string, starting with the length (UInt32) + number of chars (16Bit encoded).

## RSeDb
In older versions, the database contains also the segment information.
Offset	Name	Type	Description
0000	ID	UUID	The internal name of the database.
0010	Version	UInt32	The version of database schema.
0014	arr1	UInt16[4]
001C	created	Date	The creation date of the database.

### Version 0x10
Offset	Name	Type	Description
0024	arr3	UInt16[8]
0034	arr2	UInt16[4]
003C	modified	Date	The last modification date of the database.
0044	arr3	UInt16[12]
005C	dat3	Date
0064	uid2	UUID
0074	arr4	UInt32[2]
0078	Txt	String16
	arr5	UInt32[2]

The Remaining data contains the segment information.
### Version 0x15
Offset	Name	Type	Description
0024	arr2	UInt16[4]
002C	modified	Date	The last modification date of the database.
0034	arr3	UInt16[12]
0040	dat3	Date
0048	uid2	UUID
0058	arr4	UInt32[2]
0060	Txt	String16
	arr5	UInt32[2]

The Remaining data contains the segment information.
### Version 0x1A
Offset	Name	Type	Description
0024	arr2	UInt16[4]
002C	modified	Date	The last modification date of the database.
0034	txt2	String16	UTF-16LE encoded string
	arr3	UInt16[12]
	dat3	Date
	uid2	UUID
	u16	UInt16
	arr4	UInt32[2]
	txt	String16
	arr5	UInt32[2]
	txt3	String16
	arr6	UInt32[4]

The Remaining data contains the segment information.
### Version 0x1D
Offset	Name	Type	Description
0024	arr2	UInt16[4]
002C	modified	Date	The last modification date of the database.
0034	Comment	String	The comment of the used template.

### Version 0x1F
Offset	Name	Type	Description
0024	arr2	UInt16[4]
002C	modified	Date	The last modification date of the database.
0034	Comment	String16	The comment of the used template.

## RSeSegInfo
The segment information consists of the documents segments. Each segment consists of a set of sections:
1. Graphics
   The graphic elements of the document. It contains the 3D elements. (PmGraphicsSegment for Parts or AmGraphicsSegment for Assemblies).
2. BRep
   The boundary representation the model. Beside some metha information a complet 3D-Model is available as ACIS binary data (PmBRepSegment for Parts or AmBRepSegment for Assemblies).
3. Definition Collection:
   The “cook-book” for the model (PmDCSegment for parts, AmDcSegment for Assemblies or DlDocDCSegment for Drawings)
4. Browser:
   The browser elements (PmBrowserSegment for parts, AmBrowserSegment for assemblies or DlBrowserSegment for drawings)
5. Application:
   The application segment (PmAppSegment for parts, AmAppSegment for IAM or DlAppSegment for IDW)
6. Results:
   (PmResultSegment for parts or AmRxSegment for assemblies)
7. Nothes:
   (NBNotebookSegment in all inventor files)
8. DesignView:
   (DesignViewSegment)
9. Directory
   The directory segment (DlDirectorySegment for IDW)

Offset	Name	Type	Description
0000	Count	Number	The number of segments
	Count * Segment
	List1		The segment’s referenced objects
	List2		The segment’s referenced types

### Single segment
Offset	Name	Type	Description
	Name	String16	The name of the segment
	ID	UUID	The internal name of the segment
	RevisionRef	UUID	The reference to the RSeRevisionInfo
	value1	UInt32
	count1	UInt32
	arr1	UInt32[5]
	count2	UInt32	The number of sections
	Type	String16	The name of the type (?)
	list1		Contains the Object types
	arr2	UINT16[n]	The size of the array depends on the RSeDb version: / 0x10: n = 6 / 0x15: n = 6 / 0x1A: n = 8 / 0x1D: n = 8 / 0x1F: n = 10
	list2		Only for RSeDB version > 0x10 (!)

### Segment objects
Offset	Name	Type	Description
	revisionRef	UUID	The reference to the RSeRevisionInfo
	values	UInt8[9]
	segRef	UUID	Reference to this segment
	value1	UInt32
	value2	UInt32	Count of nodes
	Nodes	N*RSeSegNode

### Segment nodes
Offset	Name	Type	Description
	Index	UInt32
	indexList1	SInt16
	indexList2	SInt16
	values	UInt16[n]	The size of the array depends on the RSeDb version: / 0x10: n = 4 / 0x15: n = 4 / 0x1A: n = 4 / 0x1D: n = 4 / 0x1F: n = 6
	number	UInt16

## Sections
The sections are split into to file Mxxx and Bxxx. The name xxx is generic. M contains the metadata for the sections. B the binary data of each section.
### Meta information
Offset	Name	Type	Description
	txt1	UTF-16LE	RSe Meta Stream Version
	Version	UInt16	The schema version for the meta data
	arr1	UInt16[8]
	name	UTF-16LE	The name of the segment the sections belongs to
	refSegUID	UUID	The UID of the referenced segment
	arr2	UInt16[3]
	val1	UInt32	optional
	dat1	UTF-16LE	The creation date of the section
	val2	UInt32	optional
	dat2	UTF-16LE	The last modify date of the section
	data	BLOB	compressed data
	num	UINT32	Number of sections
	values	UINT32{num}	The size (BIT 0-30] and flag (BIT31) of the sections

### Binary information
Offset	Name	Type	Description
	refSegUID	UUID	The UID of the referenced segment
	n	UInt16
	data	BLOB	compressed data for all sections,
	[flags,blob,size]{num]	(UINT32,UINT8{size}[UINT32]){num}	Structure
	flags	UINT32	0x000000FF: Index of section’s type (ref. segment.secBlkTypes)
	values	UINT8{sec.size}	The raw data of each section
	secSize	UINT32	The size of the section (should be sec.size)